THE AERODYNAMICS AND PROCESS IN THE VORTEX CHAMBERS

J.J. Smulsky

Institute of Earth's Cryosphere,

625026, Tyumen, Malygin Str. 86, Russia.

Tel.:+7-3452-68-87-14 : E-mail: JSmulsky@mail.ru

This book had published in Russian at 1992 by "Science Publisher".

At present, the vortex chambers are widely used in the existing technological process and new technologies are appeared on its base. Such usage should be more effective if there are the methods of the aerodynamics and process in the vortex chambers calculation. In literature it is known separate researches of the aerodynamics and process in the vortex chambers, made by different authors. There are also the methods of the aerodynamics different sides calculation.

Suggested monograph is distinguished itself by the systematic character these problems complete set and completion of the considering. Here it is researched incompressible and compressible flow of the mono-phased medium, and two-phased medium motion as well. All problems are considered theoretically and experimentally, are given methods process calculation and its realization in the form of programs for computers, are given practical recommendations.

The monograph consists of 10 chapters. The first 6 chapters are devoted to mono-phased medium the chapters from 7 to 9 are devoted to two-phased medium, and the 10-th one - to atmosphere vortexes. In the first part the author has received numerical and analytical solutions for Navier-Stockes equations in the one-two-dimensional model of the vortex chamber. It has permitted him to create the method of the incompressible (the 5-th chapter ) and compressible (the 6-th chapter ) flow in vortex chambers calculation. The fourth chapter is devoted to the experimental researches of the vortex chamber aerodynamics, which are based on the systematical researches, generally by the author himself. The results of the experiments are tabulated and given in the appendixes. The author spared much attention to the truth of the measurement results, that is why given data can be used not only as a bank of data for the further theories but also as the based material for control of the new experiments.

Apparently, here it is for the first time considered the calculation of the compressible flow and it is received the results not only speed and pressure but for density, temperature and other parameters as well. It is of large, practical interest considered in this work the problem of vortex chambers optimization and criteria for its modeling.

In the monograph it is systematized representations on the interaction of the particle and flow in the vortex chamber and received the results for different regimes of the particle motion in the fluid. On this base it is considered the problems of gas clearing for different kinds of separators and, that is very important, it is developed the method of the separation efficiency calculation, which is given in the form of the program-me for computer. It permits to calculate the efficiency of dust separators, not resorting to its testing. It is also considered here the mechanics of rotating and weighted layers. Received methods of process calculations will permit to use more effectively vortex chambers in industrial scales.

The book will be of interest for meteorologists the results, received for tornado. The methods of the whirlpools calculation when outflow from reservoirs can be practically adopted in technique.

The monograph is written in the clear language, it abounds in experimental results and calculations on the whole and will be interest for students and specialists.

C O N T E N T S

INTRODUCTION............................................................................................................................  6

PRINCIPAL NOTATION ..............................................................................................................  9

CHAPTER  1. GENERAL STATEMENTS..................................................................................  13

1.1. Determination of the vortex chambers and its usage ......................................................  13

1.2. Concise review of research .............................................................................................  17

1.3. The swirl degree in the vortex chamber ...........................................................................  23

1.4. Creation of the swirl flow in the vortex chamber..............................................................  25

CHAPTER  2. INCOMPRESSIBLE VISCOUS FLOW IN THE VORTEX CHAMBER ............29

2.1. Flow model analysis........................................................................................................  29

2.2. One-dimensional model formulation of the task .............................................................  36

2.3. A solution for the peripheral region.................................................................................  41

2.4. A solutions in the meridian plane.....................................................................................  43

2.5. A solution for tangential velocity .....................................................................................  50

2.6. A solution for pressure......................................................................................................  53

2.7. Fields of velocity and pressure in the vortex chamber and porous pipe............................  57

2.8. About turbulent model of the flow....................................................................................  60

CHAPTER  3. METHODS OF THE VORTEX CHAMBER AERODYNAMICS

EXPERIMENTAL RESEARCH........................................................................................  61

3.1. Review of the research methods ......................................................................................  61

3.2. Sonde influence on the ratating flow ...............................................................................  63

3.3. Thin cylindrical sonde extended along diameter .............................................................  65

3.4. Turbulence influence on the cylindrical sonde measurements results .............................  68

3.5. Determination of the real error of sonde ..........................................................................  70

3.6. Determination of the tangential speed according to the pressure gradient ......................  74

3.7. Measuring of the pressure with the help of the liquid free surface ……...........................  75

3.8. Flow visualization in the vortex chamber .........................................................................  78

CHAPTER  4. EXPERIMENTAL RESEARCH OF THE VORTEX CHAMBER AERODYNAMICS…………………………………………………………………………….… 80

4.1. Geometry of the chambers ................................................................................................  80

4.2. Flow structure in vortex chamber .....................................................................................  83

4.3. Air flow rate influence ......................................................................................................  91

4.4. Outlet radius influence ......................................................................................................  97

4.5. The swirl degree influence ..............................................................................................  105

4.6. Chamber length influence ...............................................................................................  108

4.7. Exhaust height influence .................................................................................................  111

4.8. Aerodynamical resistance of the vortex chamber ...........................................................  113

CHAPTER  5. INCOMPRESSIBLE FLOW CALCULATION IN THE VORTEX CHAMBER..114

5.1. Theoretical results and experimental ones comparison ………………………………..  114

5.2. Mains experimental results analysis. Its' generalization………………………………... 120

5.3. Calculation method of the incompressible flow ...     …………………………………   125

CHAPTER  6. COMPRESSIBLE FLOW IN THE VORTEX CHAMBER ................................  129

6.1. Compressible flow some characteristic property............................................................  129

6.2. Pressure and tangential velocity .....................................................................................  130

6.3. Radial and axis velocities ...............................................................................................  135

6.4. Calculation method of the compressible flow ................................................................  140

6.5. Optimal characteristics of the vortex chamber ...............................................................  144

6.6. Criteria of the modeling the vortex chamber aerodynamics ..........................................  144

CHAPTER  7. PARTICLES MOTION IN THE VORTEX CHAMBER...................................... 146

7.1. Forces, acted on the particle ............................................................................................ 146

7.2. Stocks particle motion equations ..................................................................................... 150

7.3. Light particle motion ....................................................................................................... 153

7.4. The equation of the heavy particle motion ...................................................................... 155

7.5. The motion equations at the quadratic regime of resis-

tance law. Criteria of the particle  difference ..................................................................... 158

CHAPTER  8. PARTICLES SEPARATION IN THE VORTEX CHAMBER ............................ 161

8.1. One-dimensional model of separation ............................................................................. 161

8.2. Separating efficiency of polydispersial flow ................................................................... 165

8.3. Cyclone............................................................................................................................. 166

8.4. Anticyclone....................................................................................................................... 171

8.5. Forward flow vortex separator.......................................................................................... 175

8.6. Comparable experiments of the vortex separators............................................................ 176

CHAPTER  9. ROTATING LAYER OF PARTICLES IN THE VORTEX CHAMBER ............ 181

9.1. Experimental research of the rotating weighted layer …………………………………. 181

9.2. Rotatable layer mechanics................................................................................................ 185

9.3. Fully weighted layer mechanics....................................................................................... 189

9.4. Rotating layer usage.......................................................................................................... 192

CHAPTER 10. VORTEXES IN THE ATMOSPHERE................................................................. 196

10.1. Whirlwinds observable properties................................................................................... 196

10.2. Discharge's model of the tornado .................................................................................... 198

10.3. Model of the whirlpool at discharge from reservoir ....................................................... 199

10.3.1. The discharge with replenishment.......................................................................... 199

10.3.2. The discharge without replenishment..................................................................... 202

10.4. Circulation formation when atmosphere and discharge move relatively ........................ 206

10.5  Circulation formation at rotation of the Earth ................................................................. 208

10.6. Potential pressure when the dry atmosphere discharge ……………………………….. 210

10.7. Moist atmosphere discharge............................................................................................ 216

10.8. Mechanics, forecast and prevention of the tornado ........................................................ 220

SUMMARY .................................................................................................................................. 225

REFERENCES.............................................................................................................................. 228

APPENDIXES  ............................................................................................................................. 237

Appendix  1. The results of the numerical solution....................................................................... 237

Appendix  2. The table of speed and pressure measuring profiles ……………………………... 240

Appendix  3. Pressure profiles on the bottom of the vortex chamber with lateral injection.......... 248

Appendix  4. Pressure in the center and at the periphery in different chambers at change of flow rate .................................................................................................................................................. 250

Appendix  5. "Vortex 1" program. Incompressible flow calculation ……………………………. 253

Appendix  6. "Vortex 1" results.................................................................................................... 265

Appendix  7. "Vortex 2" program. Compressible flow calculation .............................................. 267

Appendix  8. "Vortex 2" results..................................................................................................... 280

Appendix  9. "Separ" program. Calculation of the cyclone clearing level.................................... 282

Appendix 10. "Separ" results......................................................................................................... 288

Appendix 11. "ROTLAY" program. Calculation of the rotary layer ........................................... 289

Appendix 12. "ROTLAY" results................................................................................................... 292

Appendix 13. "Weilay" program. Calculation of the fully weighted layer ................................... 293

Appendix 14. "Weilay" results....................................................................................................... 298

Appendix 15. "Discharge" program. Calculation of the water whirl-pool and its results.............. 299

The corrected in January 2010 book (Smulsky J.J. The Aerodynamics and Processes in the Vortex Chambers. - Novosibirsk: Publishers "Science". - 1992. - 301 p. (In Russian)) can be copied in a djvu-format here: http://www.ikz.ru/~smulski/Aerpro/aerpro.djvu. The computer programs to the book on the FORTRAN can be copied here: http://www.ikz.ru/~smulski/Aerpro/PrgrmAVC.rar. Information about program in Russian see:  http://www.ikz.ru/~smulski/Aerpro/ReadMe.pdf .